## Slide 1: Masterarbeit Notizen
cand. el. Simon Müller
Innovative selbstlernende Gestensteuerung im Automotivbereich
M.Sc. Simon Stock; M.Sc. Marco Stang

## Slide 2: Intel Realsense D435
Working distances:
  Min-Z: ~10cm
  Max-Z: 10m
  => 30cm – 1m in car should be ok
Depth:
  Res: 1280 x 720@90fps
  FOV: 87°±3° x 58°±1° x 95°±3°
RGB:
  Res: 1920x1080@30fps
  FOV: 69.4° x 42.5° x 77° (+/- 3°)
  => Projection needed!*
Projection
  * https://github.com/IntelRealSense/librealsense/tree/development/examples/align
  https://github.com/IntelRealSense/librealsense/blob/master/wrappers/python/examples/align-depth2color.py

## Slide 3: Two-step sequence
Input Frame
RGB
Input Frame
Depth
CNN
Intermediate representation
(„Skeleton“)
Classifier
(LSTM?)
Gesture
Class
Input Frame
RGB
Input Frame
Depth
CNN
Intermediate representation
(„Skeleton“)
t
t+n
…
No gesture
Pose estimation
Gesture classification
Lowpass

## Slide 4: Pose Estimation
 | Estimate Joint angles | Estimate Joint position
How | CNN | CNN
+ | Dimensional reduction Easily understandable representation | Dimensional reduction Semi-Automatic labeling with previous work Angles still calculatable
- | How to lable? Manual labeling almost impossible -> Synthetic data? | How do you label occluded joints?

## Slide 5: Datasets Hand Pose Estimation
 | FHAD | BigHands 2/2m | cvpr15_MSRAHandGestureDB | FreiHAND | Imperial College London | NvGesture
+ | Skeleton annotations (joint locations) RGBD | Relatively large dataset Well curated because it was/is used in competition | Skeleton annotations (joint locations) |  |  | Relatively large Many subjects
- | Sensors + tape on hands make RGB images risky to work with |  | No RGB |  | No RGB Low contrast | No pose labels

## Slide 6: Data augmentation (Núñez et al. 2018, S.84)
Various possibilities:
  Scale
  Shift
  Time interpolation (Hard to do for images)
  Noise

## Slide 7: Problem: execution time
Many networks take >30ms,
some even need preprocessing (hand segmentation)
 Tradeoff betwen precision and speed

## Slide 8: Problem: Coordinate systems and camera models
Training data was recorded with different cameras  Camera intrinsics will vary between training/application
Most activation functions cut negative values  Normalization required
  BUT: Gestures can contain every possible movement  Cropping/Normalization around fixed point of hand (e.g. palm as in [1]) not possible
[1] Malik, Jameel; Elhayek, Ahmed; Stricker, Didier (2018): Structure-Aware 3D Hand Pose Regression from a Single Depth Image. In: Patrick Bourdot, Sue Cobb, Victoria Interrante, Hirokazu kato und Didier Stricker (Hg.): Virtual reality and augmented reality. 15th EuroVR International Conference, EuroVR 2018, London, UK, October 22–23, 2018 : proceedings, Bd. 11162. Cham: Springer (Lecture Notes in Computer Science, 11162), S. 3–17.

## Slide 9: Unified Datset Format
Skeleton Coordinates in CAMERA coordinates (apply intrinsics but not extrinsics!)
  Allows to detect movement towards camera etc but does not depend on camera orientation
21 Joints
Skeleton joint order:
  FHAD compatible: ["wrist", "tmcp", "imcp", "mmcp", "rmcp", "pmcp", "tpip", "tdip", "ttip", "ipip", "idip", "itip", "mpip", "mdip", "mtip", "rpip", "rdip", "rtip", "ppip", "pdip", "ptip"]
Depth image, 640x480
Tfrecords of img/skel pairs. Reduces epoch times by a factor of 10-20

## Slide 10: One-Shot training
New data through data augmentation (Núñez et al. 2018, S.84)
Siamese networks
  Compare input data with known classes
  Output is similarity factor
   Triple loss function!

## Slide 11: Sources
Núñez, Juan C.; Cabido, Raúl; Pantrigo, Juan J.; Montemayor, Antonio S.; Vélez, José F. (2018): Convolutional Neural Networks and Long Short-Term Memory for skeleton-based human activity and hand gesture recognition. In: Pattern Recognition 76, S. 80–94. DOI: 10.1016/j.patcog.2017.10.033.
IEEE International Conference on Automatic Face and Gesture Recognition; Institute of Electrical and Electronics Engineers; FG (2018): 13th IEEE International Conference on Automatic Face and Gesture Recognition. FG 2018 : 15-19 May 2018, Xi'an, China : proceedings. 2018 13th IEEE International Conference on Automatic Face & Gesture Recognition (FG 2018). Xi'an, 5/15/2018 - 5/19/2018. Piscataway, NJ: IEEE.
2013 IEEE International Conference on Computer Vision. 1-8 December 2013 (2014). 2013 IEEE International Conference on Computer Vision (ICCV). Sydney, Australia, 12/1/2013 - 12/8/2013. New York: IEEE.
Institute of Electrical and Electronics Engineers; IEEE Conference on Computer Vision and Pattern Recognition; CVPR (2015): 2015 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). - 12 June 2015, Boston, MA. 2015 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Boston, MA, USA, 6/7/2015 - 6/12/2015. Piscataway, NJ: IEEE.
2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR) (2016 - 2016). 2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Las Vegas, NV, USA, 27.06.2016 - 30.06.2016: IEEE.

## Slide 12: Sources
IEEE Conference on Computer Vision and Pattern Recognition; Institute of Electrical and Electronics Engineers; CVPR (2016): 29th IEEE Conference on Computer Vision and Pattern Recognition. CVPR 2016 : proceedings : 26 June-1 July 2016, Las Vegas, Nevada. Unter Mitarbeit von Růžena Bajcsy, Fei-Fei Li und Tinne Tuytelaars. 2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Las Vegas, NV, USA, 6/27/2016 - 6/30/2016. Piscataway, NJ: IEEE.
IEEE Conference on Computer Vision and Pattern Recognition; Institute of Electrical and Electronics Engineers; IEEE/CVF Conference on Computer Vision and Pattern Recognition; CVPR (2017): 30th IEEE Conference on Computer Vision and Pattern Recognition. CVPR 2017 : 21-26 July 2016, Honolulu, Hawaii : proceedings. Unter Mitarbeit von Rama Chellappa, Zhengyou Zhang und Anthony Hoogs. 2017 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Honolulu, HI, 7/21/2017 - 7/26/2017. Piscataway, NJ: IEEE.

## Slide 13: Sources
Hernandez Ruiz, Alejandro; Porzi, Lorenzo; Rota Bulò, Samuel; Moreno-Noguer, Francesc (2017): 3D CNNs on Distance Matrices for Human Action Recognition. In: Qiong Liu, Rainer Lienhart, Haohong Wang, Sheng-Wei "Kuan-Ta" Chen, Susanne Boll, Phoebe Chen et al. (Hg.): MM'17. Proceedings of the 2017 ACM Multimedia Conference : October 23-27, 2017, Amsterdam, the Netherlands. Unter Mitarbeit von Qiong Liu, Rainer Lienhart und Haohong Wang. the 2017 ACM. Mountain View, California, USA, 10/23/2017 - 10/27/2017. ACM Multimedia Conference; Association for Computing Machinery; ACM Multimedia; MM. New York, NY, USA: ACM Association for Computing Machinery, S. 1087–1095.
Ge, Liuhao; Liang, Hui; Yuan, Junsong; Thalmann, Daniel (2017): 3D Convolutional Neural Networks for Efficient and Robust Hand Pose Estimation from Single Depth Images. In: 30th IEEE Conference on Computer Vision and Pattern Recognition. CVPR 2017 : 21-26 July 2016, Honolulu, Hawaii : proceedings. Unter Mitarbeit von Rama Chellappa, Zhengyou Zhang und Anthony Hoogs. 2017 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Honolulu, HI, 7/21/2017 - 7/26/2017. IEEE Conference on Computer Vision and Pattern Recognition; Institute of Electrical and Electronics Engineers; IEEE/CVF Conference on Computer Vision and Pattern Recognition; CVPR. Piscataway, NJ: IEEE, S. 5679–5688.
Zhang, Jiawei; Jiao, Jianbo; Chen, Mingliang; Qu, Liangqiong; Xu, Xiaobin; Yang, Qingxiong (2016): 3D Hand Pose Tracking and Estimation Using Stereo Matching. Online verfügbar unter http://arxiv.org/pdf/1610.07214v1.

## Slide 14: Sources
Liu, Zhi; Zhang, Chenyang; Tian, Yingli (2016): 3D-based Deep Convolutional Neural Network for action recognition with depth sequences. In: Image and Vision Computing 55, S. 93–100. DOI: 10.1016/j.imavis.2016.04.004.
Hoang, Nguyen Ngoc; Lee, Guee-Sang; Kim, Soo-Hyung; Yang, Hyung-Jeong (2018): A Real-time Multimodal Hand Gesture Recognition via 3D Convolutional Neural Network and Key Frame Extraction. In: Unknown (Hg.): Proceedings of the 2018 International Conference on Machine Learning and Machine Intelligence - MLMI2018. the 2018 International Conference. Ha Noi, Viet Nam, 28.09.2018 - 30.09.2018. New York, New York, USA: ACM Press, S. 32–37.
Farooq, Adnan; Won, Chee Sun (2015): A Survey of Human Action Recognition Approaches that use an RGB-D Sensor. In: IEIE Transactions on Smart Processing and Computing 4 (4), S. 281–290. DOI: 10.5573/IEIESPC.2015.4.4.281.
Wang, Pichao; Li, Wanqing; Gao, Zhimin; Zhang, Jing; Tang, Chang; Ogunbona, Philip O. (2016): Action Recognition From Depth Maps Using Deep Convolutional Neural Networks. In: IEEE Trans. Human-Mach. Syst. 46 (4), S. 498–509. DOI: 10.1109/THMS.2015.2504550.
Xin, Miao; Zhang, Hong; Wang, Helong; Sun, Mingui; Yuan, Ding (2016): ARCH: Adaptive recurrent-convolutional hybrid networks for long-term action recognition. In: Neurocomputing 178, S. 87–102. DOI: 10.1016/j.neucom.2015.09.112.

## Slide 15: Sources
Szeliski, Richard (1989): Bayesian modeling of uncertainty in low-level vision (The Kluwer international series in engineering and computer science).
Yuan, Shanxin; Ye, Qi; Stenger, Bjorn; Jain, Siddhant; Kim, Tae-Kyun (2017): BigHand2.2M Benchmark: Hand Pose Dataset and State of the Art Analysis. Online verfügbar unter http://arxiv.org/pdf/1704.02612v2.
Sun, Xiao; Wei, Yichen; Liang, Shuang; Tang, Xiaoou; Sun, Jian (2015): Cascaded hand pose regression. In: 2015 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). - 12 June 2015, Boston, MA. 2015 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Boston, MA, USA, 6/7/2015 - 6/12/2015. Institute of Electrical and Electronics Engineers; IEEE Conference on Computer Vision and Pattern Recognition; CVPR. Piscataway, NJ: IEEE, S. 824–832.
Hafiz, Abdul Rahman; Al-Nuaimi, Ahmed Yarub; Amin, Md. Faijul; Murase, Kazuyuki (2015): Classification of Skeletal Wireframe Representation of Hand Gesture Using Complex-Valued Neural Network. In: Neural Processing Letters 42 (3), S. 649–664. DOI: 10.1007/s11063-014-9379-0.
Szeliski, Richard (2011): Computer vision. Algorithms and applications (Texts in computer science).

## Slide 16: Sources
Szeliski, Richard (2011): Computer Vision. Algorithms and Applications. London: Springer London (Texts in computer science).
Szeliski, Richard (2010): Computer Vision. Algorithms and Applications. 1. Aufl. Guildford, Surrey: Springer London (Texts in computer science).
Cremers, Daniel; Reid, Ian; Saito, Hideo; Yang, Ming-Hsuan (Hg.) (2015): Computer Vision -- ACCV 2014. Cham: Springer International Publishing (Lecture Notes in Computer Science).
Cremers, Daniel; Reid, Ian; Saito, Hideo; Yang, Ming-Hsuan (Hg.) (2015): Computer Vision -- ACCV 2014. Cham: Springer International Publishing (Lecture Notes in Computer Science).
Fitzgibbon, Andrew; Lazebnik, Svetlana; Perona, Pietro; Sato, Yoichi; Schmid, Cordelia (Hg.) (2012): Computer vision - ECCV 2012. 12th European Conference on Computer Vision, Florence, Italy, October 7 - 13, 2012 ; proceedings, part VI. ECCV; European Conference on Computer Vision. Berlin: Springer (Lecture Notes in Computer Science, 7577).

## Slide 17: Sources
Núñez, Juan C.; Cabido, Raúl; Pantrigo, Juan J.; Montemayor, Antonio S.; Vélez, José F. (2018): Convolutional Neural Networks and Long Short-Term Memory for skeleton-based human activity and hand gesture recognition. In: Pattern Recognition 76, S. 80–94. DOI: 10.1016/j.patcog.2017.10.033.
Li, Yuan; Wang, Xinggang; Liu, Wenyu; Feng, Bin (2018): Deep attention network for joint hand gesture localization and recognition using static RGB-D images. In: Information Sciences 441, S. 66–78. DOI: 10.1016/j.ins.2018.02.024.
Pfister, Tomas; Simonyan, Karen; Charles, James; Zisserman, Andrew (2015): Deep Convolutional Neural Networks for Efficient Pose Estimation in Gesture Videos. In: Daniel Cremers, Ian Reid, Hideo Saito und Ming-Hsuan Yang (Hg.): Computer Vision -- ACCV 2014, Bd. 9003. Cham: Springer International Publishing (Lecture Notes in Computer Science), S. 538–552.
Di Wu; Pigou, Lionel; Kindermans, Pieter-Jan; Le, Nam Do-Hoang; Shao, Ling; Dambre, Joni; Odobez, Jean-Marc (2016): Deep Dynamic Neural Networks for Multimodal Gesture Segmentation and Recognition. In: IEEE transactions on pattern analysis and machine intelligence 38 (8), S. 1583–1597. DOI: 10.1109/TPAMI.2016.2537340.
Devineau, Guillaume; Moutarde, Fabien; Xi, Wang; Yang, Jie (2018): Deep Learning for Hand Gesture Recognition on Skeletal Data. In: 13th IEEE International Conference on Automatic Face and Gesture Recognition. FG 2018 : 15-19 May 2018, Xi'an, China : proceedings. 2018 13th IEEE International Conference on Automatic Face & Gesture Recognition (FG 2018). Xi'an, 5/15/2018 - 5/19/2018. IEEE International Conference on Automatic Face and Gesture Recognition; Institute of Electrical and Electronics Engineers; FG. Piscataway, NJ: IEEE, S. 106–113.

## Slide 18: Sources
Malik, Jameel; Elhayek, Ahmed; Nunnari, Fabrizio; Varanasi, Kiran; Tamaddon, Kiarash; Heloir, Alexis; Stricker, Didier (2018): DeepHPS: End-to-end Estimation of 3D Hand Pose and Shape by Learning from Synthetic Depth. Online verfügbar unter http://arxiv.org/pdf/1808.09208v1.
Yuan, Shanxin; Garcia-Hernando, Guillermo; Stenger, Bjorn; Moon, Gyeongsik; Chang, Ju Yong; Lee, Kyoung Mu et al. (2017): Depth-Based 3D Hand Pose Estimation: From Current Achievements to Future Goals. Online verfügbar unter http://arxiv.org/pdf/1712.03917v2.
Wu, Chih-Hung; Chen, Wei-Lun; Lin, Chang Hong (2016): Depth-based hand gesture recognition. In: Multimed Tools Appl 75 (12), S. 7065–7086. DOI: 10.1007/s11042-015-2632-3.
Supančič, James Steven; Rogez, Grégory; Yang, Yi; Shotton, Jamie; Ramanan, Deva (2018): Depth-Based Hand Pose Estimation: Methods, Data, and Challenges. In: Int J Comput Vis 126 (11), S. 1180–1198. DOI: 10.1007/s11263-018-1081-7.
Melax, Stan; Keselman, Leonid; Orsten, Sterling (2017): Dynamics Based 3D Skeletal Hand Tracking. Online verfügbar unter http://arxiv.org/pdf/1705.07640v1.

## Slide 19: Sources
Oikonomidis, Iason; Kyriazis, Nikolaos; Argyros, Antonis (2011): Efficient model-based 3D tracking of hand articulations using Kinect. In: Jesse Hoey (Hg.): Proceedings of the British Machine Vision Conference 2011. BMVC 2011, the 22nd British Machine Vision Conference, University of Dundee, 29 August-2 September 2011. British Machine Vision Conference 2011. Dundee. British Machine Vision Conference; BMVC. Durham: BMVA Press, 101.1-101.11.
Kang, Sing Bing; Szeliski, Richard: Extracting View-Dependent Depth Maps from a Collection of Images.
Garcia-Hernando, Guillermo; Yuan, Shanxin; Baek, Seungryul; Kim, Tae-Kyun (2017): First-Person Hand Action Benchmark with RGB-D Videos and 3D Hand Pose Annotations. Online verfügbar unter http://arxiv.org/pdf/1704.02463v2.
Ohn-Bar, Eshed; Trivedi, Mohan Manubhai (2014): Hand Gesture Recognition in Real Time for Automotive Interfaces: A Multimodal Vision-Based Approach and Evaluations. In: IEEE Trans. Intell. Transport. Syst. 15 (6), S. 2368–2377. DOI: 10.1109/TITS.2014.2337331.
Simon, Tomas; Joo, Hanbyul; Matthews, Iain; Sheikh, Yaser (2017): Hand Keypoint Detection in Single Images using Multiview Bootstrapping. Online verfügbar unter http://arxiv.org/pdf/1704.07809v1.

## Slide 20: Sources
Keskin, Cem; Kıraç, Furkan; Kara, Yunus Emre; Akarun, Lale (2012): Hand Pose Estimation and Hand Shape Classification Using Multi-layered Randomized Decision Forests. In: Andrew Fitzgibbon, Svetlana Lazebnik, Pietro Perona, Yoichi Sato und Cordelia Schmid (Hg.): Computer vision - ECCV 2012. 12th European Conference on Computer Vision, Florence, Italy, October 7 - 13, 2012 ; proceedings, part VI, Bd. 7577. Berlin: Springer (Lecture Notes in Computer Science, 7577), S. 852–863.
Hampali, Shreyas; Oberweger, Markus; Rad, Mahdi; Lepetit, Vincent (2019): HO-3D: A Multi-User, Multi-Object Dataset for Joint 3D Hand-Object Pose Estimation. Online verfügbar unter http://arxiv.org/pdf/1907.01481v1.
Poier, Georg; Roditakis, Konstantinos; Schulter, Samuel; Michel, Damien; Bischof, Horst; Argyros, Antonis A. (2015): Hybrid One-Shot 3D Hand Pose Estimation by Exploiting Uncertainties. In: Xianghua Xie, Mark W. Jones und Gary K. L. Tam (Hg.): Proceedings of the British Machine Vision Conference 2015. BMVC 2015, 7-10 September, Swansea, UK. British Machine Vision Conference 2015. Swansea. British Machine Vision Conference; BMVC. Durham: BMVA Press, 182.1-182.14.
Institute of Electrical and Electronics Engineers; IEEE Computer Society; IEEE Conference on Computer Vision and Pattern Recognition; CVPR (2013): IEEE Conference on Computer Vision and Pattern Recognition (CVPR), 2013. 23 - 28 June 2013, Portland, Oregon, USA ; proceedings. 2013 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Portland, OR, USA, 6/23/2013 - 6/28/2013. Piscataway, NJ: IEEE.
Szeliski, Richard (2006): Image alignment and stitching. A Tutorial. Hanover Mass. u.a.: Now Publ (Foundations and trends in computer graphics and vision, 2,1).

## Slide 21: Sources
Sridhar, Srinath; Oulasvirta, Antti; Theobalt, Christian (2013): Interactive Markerless Articulated Hand Motion Tracking using RGB and Depth Data. In: Proceedings of the IEEE International Conference on Computer Vision (ICCV). Online verfügbar unter http://handtracker.mpi-inf.mpg.de/projects/handtracker_iccv2013/.
Fei-Fei, Li: Knowledge transfer in learning to recognize visual objects classes.
Zimmermann, Christian; Brox, Thomas (2017): Learning to Estimate 3D Hand Pose from Single RGB Images. Online verfügbar unter http://arxiv.org/pdf/1705.01389v3.
Liu, Qiong; Lienhart, Rainer; Wang, Haohong; Chen, Sheng-Wei "Kuan-Ta"; Boll, Susanne; Chen, Phoebe et al. (Hg.) (2017): MM'17. Proceedings of the 2017 ACM Multimedia Conference : October 23-27, 2017, Amsterdam, the Netherlands. Unter Mitarbeit von Qiong Liu, Rainer Lienhart und Haohong Wang. the 2017 ACM. Mountain View, California, USA, 10/23/2017 - 10/27/2017. ACM Multimedia Conference; Association for Computing Machinery; ACM Multimedia; MM. New York, NY, USA: ACM Association for Computing Machinery.
Lin, John; Wu, Ying; Huang, T. S. (2000): Modeling the constraints of human hand motion. In: Proceedings, Workshop on Human Motion. 7-8 December 2000, Austin, Texas. Workshop on Human Motion. Los Alamitos, CA, USA, 7-8 Dec. 2000. Workshop on Human Motion; IEEE Computer Society. Los Alamitos, Calif: IEEE Computer Society, S. 121–126.

## Slide 22: Sources
Patrona, Fotini; Chatzitofis, Anargyros; Zarpalas, Dimitrios; Daras, Petros (2018): Motion analysis: Action detection, recognition and evaluation based on motion capture data. In: Pattern Recognition 76, S. 612–622. DOI: 10.1016/j.patcog.2017.12.007.
Maddison, Chris J.; Huang, Aja; Sutskever, Ilya; Silver, David (2014): Move Evaluation in Go Using Deep Convolutional Neural Networks. Online verfügbar unter http://arxiv.org/pdf/1412.6564v2.
Stark, Michael: On knowledge transfer in object class recognition. Darmstadt, Techn. Univ., Diss., 2010.
Molchanov, Pavlo; Yang, Xiaodong; Gupta, Shalini; Kim, Kihwan; Tyree, Stephen; Kautz, Jan (2016 - 2016): Online Detection and Classification of Dynamic Hand Gestures with Recurrent 3D Convolutional Neural Networks. In: 2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). 2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Las Vegas, NV, USA, 27.06.2016 - 30.06.2016: IEEE, S. 4207–4215.
Li, Cheng; Kitani, Kris M. (2013): Pixel-Level Hand Detection in Ego-centric Videos. In: IEEE Conference on Computer Vision and Pattern Recognition (CVPR), 2013. 23 - 28 June 2013, Portland, Oregon, USA ; proceedings. 2013 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Portland, OR, USA, 6/23/2013 - 6/28/2013. Institute of Electrical and Electronics Engineers; IEEE Computer Society; IEEE Conference on Computer Vision and Pattern Recognition; CVPR. Piscataway, NJ: IEEE, S. 3570–3577.

## Slide 23: Sources
Proceedings IEEE Virtual Reality 2001 (2001). IEEE Virtual Reality 2001. Yokohama, Japan, 13-17 March 2001: IEEE Comput. Soc.
Proceedings IEEE Virtual Reality 2001 (2001). IEEE Virtual Reality 2001. Yokohama, Japan, 13-17 March 2001: IEEE Comput. Soc.
Unknown (Hg.) (2018): Proceedings of the 2018 International Conference on Machine Learning and Machine Intelligence - MLMI2018. the 2018 International Conference. Ha Noi, Viet Nam, 28.09.2018 - 30.09.2018. New York, New York, USA: ACM Press.
Proceedings of the 5th international conference on devlopment and learning ICDL 2006. Indiana University, Bloomington, IN : May 31 - June 3rd, 2006 (2006). [Bloomington, Ind.]: Department of Psychological and Brain Sciences, Indiana University.
Hoey, Jesse (Hg.) (2011): Proceedings of the British Machine Vision Conference 2011. BMVC 2011, the 22nd British Machine Vision Conference, University of Dundee, 29 August-2 September 2011. British Machine Vision Conference 2011. Dundee. British Machine Vision Conference; BMVC. Durham: BMVA Press.

## Slide 24: Sources
Xie, Xianghua; Jones, Mark W.; Tam, Gary K. L. (Hg.) (2015): Proceedings of the British Machine Vision Conference 2015. BMVC 2015, 7-10 September, Swansea, UK. British Machine Vision Conference 2015. Swansea. British Machine Vision Conference; BMVC. Durham: BMVA Press.
Proceedings of the IEEE International Conference on Computer Vision (ICCV) (2013).
Workshop on Human Motion; IEEE Computer Society (2000): Proceedings, Workshop on Human Motion. 7-8 December 2000, Austin, Texas. Workshop on Human Motion. Los Alamitos, CA, USA, 7-8 Dec. 2000. Los Alamitos, Calif: IEEE Computer Society.
Ge, Liuhao; Liang, Hui; Yuan, Junsong; Thalmann, Daniel (2019): Real-Time 3D Hand Pose Estimation with 3D Convolutional Neural Networks. In: IEEE transactions on pattern analysis and machine intelligence 41 (4), S. 956–970. DOI: 10.1109/TPAMI.2018.2827052.
Tang, Danhang; Yu, Tsz-Ho; Kim, Tae-Kyun (2014): Real-Time Articulated Hand Pose Estimation Using Semi-supervised Transductive Regression Forests. In: 2013 IEEE International Conference on Computer Vision. 1-8 December 2013. 2013 IEEE International Conference on Computer Vision (ICCV). Sydney, Australia, 12/1/2013 - 12/8/2013. New York: IEEE, S. 3224–3231.

## Slide 25: Sources
Tompson, Jonathan; Stein, Murphy; Lecun, Yann; Perlin, Ken (2014): Real-Time Continuous Pose Recovery of Human Hands Using Convolutional Networks. In: ACM Trans. Graph. 33 (5), S. 1–10. DOI: 10.1145/2629500.
Köpüklü, Okan; Gunduz, Ahmet; Kose, Neslihan; Rigoll, Gerhard (2019): Real-time Hand Gesture Detection and Classification Using Convolutional Neural Networks. Online verfügbar unter http://arxiv.org/pdf/1901.10323v2.
Lu, Bao-Liang; Zhang, Liqing; Kwok, James; Hafiz, Abdul Rahman; Amin, Md. Faijul; Murase, Kazuyuki (Hg.) (2011): Real-Time Hand Gesture Recognition Using Complex-Valued Neural Network (CVNN). Neural Information Processing. Berlin, Heidelberg: Springer Berlin Heidelberg.
Shotton, Jamie; Fitzgibbon, Andrew; Blake, Andrew; Kipman, Alex; Finocchio, Mark; Moore, Bob; Sharp, Toby (2011): Real-Time Human Pose Recognition in Parts from a Single Depth Image. Online verfügbar unter https://www.microsoft.com/en-us/research/wp-content/uploads/2016/02/BodyPartRecognition.pdf.
Sato, Y.; Saito, M.; Koike, H. (2001): Real-time input of 3D pose and gestures of a user's hand and its applications for HCI. In: Proceedings IEEE Virtual Reality 2001. IEEE Virtual Reality 2001. Yokohama, Japan, 13-17 March 2001: IEEE Comput. Soc, S. 79–86.

## Slide 26: Sources
Uni Freiburg: Rendered Handpose Dataset: Uni Freiburg. Online verfügbar unter https://lmb.informatik.uni-freiburg.de/resources/datasets/RenderedHandposeDataset.en.html.
Ge, Liuhao; Liang, Hui; Yuan, Junsong; Thalmann, Daniel (2016): Robust 3D Hand Pose Estimation in Single Depth Images: from Single-View CNN to Multi-View CNNs. Online verfügbar unter http://arxiv.org/pdf/1606.07253v3.
Malik, Jameel; Elhayek, Ahmed; Stricker, Didier (2017): Simultaneous Hand Pose and Skeleton Bone-Lengths Estimation from a Single Depth Image. Online verfügbar unter http://arxiv.org/pdf/1712.03121v1.
Li, Yong; He, Zihang; Ye, Xiang; He, Zuguo; Han, Kangrong (2019): Spatial temporal graph convolutional networks for skeleton-based dynamic hand gesture recognition. In: J Image Video Proc. 2019 (1), S. 404. DOI: 10.1186/s13640-019-0476-x.
Jones, Michael J.; Rehg, James M. (2002): Statistical Color Models with Application to Skin Detection. In: Int J Comput Vis 46 (1), S. 81–96. DOI: 10.1023/A:1013200319198.

## Slide 27: Sources
Scharstein, Daniel; Szeliski, Richard: Stereo Matching with Nonlinear Diffusion.
Malik, Jameel; Elhayek, Ahmed; Stricker, Didier (2018): Structure-Aware 3D Hand Pose Regression from a Single Depth Image. In: Patrick Bourdot, Sue Cobb, Victoria Interrante, Hirokazu kato und Didier Stricker (Hg.): Virtual reality and augmented reality. 15th EuroVR International Conference, EuroVR 2018, London, UK, October 22–23, 2018 : proceedings, Bd. 11162. Cham: Springer (Lecture Notes in Computer Science, 11162), S. 3–17.
Yuan, Shanxin; Ye, Qi; Garcia-Hernando, Guillermo; Kim, Tae-Kyun (2017): The 2017 Hands in the Million Challenge on 3D Hand Pose Estimation. Online verfügbar unter http://arxiv.org/pdf/1707.02237v1.
Bourdot, Patrick; Cobb, Sue; Interrante, Victoria; kato, Hirokazu; Stricker, Didier (Hg.) (2018): Virtual reality and augmented reality. 15th EuroVR International Conference, EuroVR 2018, London, UK, October 22–23, 2018 : proceedings. Springer International Publishing AG; EuroVR. Cham: Springer (Lecture Notes in Computer Science, 11162).

## Slide 28: Masterfolie (über: Ansicht – Master – Folienmaster)
Die Masterfolie wird genutzt, um grundlegende Elemente der Präsentation festzulegen und ggf. zu ändern.
Folgende Elemente können Sie in der Normalansicht individuell eintragen:
  Inhaltsbereich:
    Präsentationsüberschrift
    Unterüberschrift
    Fakultätsbezeichnung
    Bildaustausch (graue Lasche am rechten Folienrand – zum leichteren Austausch)
  Fußzeile (über: Ansicht – Kopf- und Fußzeile)

## Slide 29: Folientitel: Arial 24pt fett 2-zeilig: Arial 20pt fett
Fließtext: Arial 24pt regular
Fußzeile: Arial 9pt regular
Seitenzahl: Arial 9pt fett
Aufzählungspunkte, falls nicht auf Folie vorhanden:
  Format – Nummerierung- und Aufzählungszeichen – Bild – Importieren
  Die Datei „kit-point.png“ auswählen
  Größe: „70% vom Text“
Farben:
  Sind bereits voreingestellt. Sie erhalten automatisch die KIT-Farbpalette

## Slide 30: Generelle Hinweise
Das Foliendesign sollte nicht geändert werden
Wenn Sie aus einem anderen Office-Programm Texte kopieren, wird Powerpoint die Formatierungen beibehalten. Hier müssen Sie die Texte evtl. neu formatieren.
Grundlegende Elemente wie diese im grauen KIT-Rahmen, das KIT-Logo oder die Platzhalter sollten in der Position nicht verändert oder gelöscht werden.

## Slide 31: Tipps zur Verwendung von Powerpoint
Seitenaufbau
  Text und Grafiken: Diese Elemente sollten gezielt und zurückhaltend eingesetzt werden. Empfohlen werden zehn Worte pro Zeile und fünf Zeilen pro Folie.
  Zahlen und Daten Effektive PowerPoint-Präsentationen enthalten wenig Zahlen: ausführliche Daten können Sie nach der Präsentation auf Handouts verteilen.