## Slide 1: Masterarbeit Notizen
cand. el. Simon Müller
Innovative selbstlernende Gestensteuerung im Automotivbereich
M.Sc. Simon Stock; M.Sc. Marco Stang

## Slide 2: Intel Realsense D435
Working distances:
  Min-Z: ~10cm
  Max-Z: 10m
  => 30cm – 1m in car should be ok
Depth:
  Res: 1280 x 720@90fps
  FOV: 87°±3° x 58°±1° x 95°±3°
RGB:
  Res: 1920x1080@30fps
  FOV: 69.4° x 42.5° x 77° (+/- 3°)
  => Projection needed!*
Projection
  * https://github.com/IntelRealSense/librealsense/tree/development/examples/align
  https://github.com/IntelRealSense/librealsense/blob/master/wrappers/python/examples/align-depth2color.py

## Slide 3: Two-step sequence
Input Frame
RGB
Input Frame
Depth
CNN
Intermediate representation
(„Skeleton“)
Classifier
(LSTM?)
Gesture
Class
Input Frame
RGB
Input Frame
Depth
CNN
Intermediate representation
(„Skeleton“)
t
t+n
…
No gesture
Pose estimation
Gesture classification
Lowpass

## Slide 4: Pose Estimation
 | Estimate Joint angles | Estimate Joint position
How | CNN | CNN
+ | Dimensional reduction Easily understandable representation | Dimensional reduction Semi-Automatic labeling with previous work Angles still calculatable
- | How to lable? Manual labeling almost impossible -> Synthetic data? | How do you label occluded joints?

## Slide 5: Datasets Hand Pose Estimation
 | FHAD | BigHands 2/2m | cvpr15_MSRAHandGestureDB | FreiHAND | Imperial College London | NvGesture
+ | Skeleton annotations (joint locations) RGBD | Relatively large dataset Well curated because it was/is used in competition | Skeleton annotations (joint locations) |  |  | Relatively large Many subjects
- | Sensors + tape on hands make RGB images risky to work with |  | No RGB |  | No RGB Low contrast | No pose labels

## Slide 6: Data augmentation (Núñez et al. 2018, S.84)
Various possibilities:
  Scale
  Shift
  Time interpolation (Hard to do for images)
  Noise

## Slide 7: One-Shot training
New data through data augmentation (Núñez et al. 2018, S.84)

## Slide 8: Sources
Núñez, Juan C.; Cabido, Raúl; Pantrigo, Juan J.; Montemayor, Antonio S.; Vélez, José F. (2018): Convolutional Neural Networks and Long Short-Term Memory for skeleton-based human activity and hand gesture recognition. In: Pattern Recognition 76, S. 80–94. DOI: 10.1016/j.patcog.2017.10.033.
IEEE International Conference on Automatic Face and Gesture Recognition; Institute of Electrical and Electronics Engineers; FG (2018): 13th IEEE International Conference on Automatic Face and Gesture Recognition. FG 2018 : 15-19 May 2018, Xi'an, China : proceedings. 2018 13th IEEE International Conference on Automatic Face & Gesture Recognition (FG 2018). Xi'an, 5/15/2018 - 5/19/2018. Piscataway, NJ: IEEE.
2013 IEEE International Conference on Computer Vision. 1-8 December 2013 (2014). 2013 IEEE International Conference on Computer Vision (ICCV). Sydney, Australia, 12/1/2013 - 12/8/2013. New York: IEEE.
Institute of Electrical and Electronics Engineers; IEEE Conference on Computer Vision and Pattern Recognition; CVPR (2015): 2015 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). - 12 June 2015, Boston, MA. 2015 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Boston, MA, USA, 6/7/2015 - 6/12/2015. Piscataway, NJ: IEEE.
2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR) (2016 - 2016). 2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Las Vegas, NV, USA, 27.06.2016 - 30.06.2016: IEEE.

## Slide 9: Sources
IEEE Conference on Computer Vision and Pattern Recognition; Institute of Electrical and Electronics Engineers; CVPR (2016): 29th IEEE Conference on Computer Vision and Pattern Recognition. CVPR 2016 : proceedings : 26 June-1 July 2016, Las Vegas, Nevada. Unter Mitarbeit von Růžena Bajcsy, Fei-Fei Li und Tinne Tuytelaars. 2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Las Vegas, NV, USA, 6/27/2016 - 6/30/2016. Piscataway, NJ: IEEE.
IEEE Conference on Computer Vision and Pattern Recognition; Institute of Electrical and Electronics Engineers; IEEE/CVF Conference on Computer Vision and Pattern Recognition; CVPR (2017): 30th IEEE Conference on Computer Vision and Pattern Recognition. CVPR 2017 : 21-26 July 2016, Honolulu, Hawaii : proceedings. Unter Mitarbeit von Rama Chellappa, Zhengyou Zhang und Anthony Hoogs. 2017 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Honolulu, HI, 7/21/2017 - 7/26/2017. Piscataway, NJ: IEEE.

## Slide 10: Sources
Hernandez Ruiz, Alejandro; Porzi, Lorenzo; Rota Bulò, Samuel; Moreno-Noguer, Francesc (2017): 3D CNNs on Distance Matrices for Human Action Recognition. In: Qiong Liu, Rainer Lienhart, Haohong Wang, Sheng-Wei "Kuan-Ta" Chen, Susanne Boll, Phoebe Chen et al. (Hg.): MM'17. Proceedings of the 2017 ACM Multimedia Conference : October 23-27, 2017, Amsterdam, the Netherlands. Unter Mitarbeit von Qiong Liu, Rainer Lienhart und Haohong Wang. the 2017 ACM. Mountain View, California, USA, 10/23/2017 - 10/27/2017. ACM Multimedia Conference; Association for Computing Machinery; ACM Multimedia; MM. New York, NY, USA: ACM Association for Computing Machinery, S. 1087–1095.
Ge, Liuhao; Liang, Hui; Yuan, Junsong; Thalmann, Daniel (2017): 3D Convolutional Neural Networks for Efficient and Robust Hand Pose Estimation from Single Depth Images. In: 30th IEEE Conference on Computer Vision and Pattern Recognition. CVPR 2017 : 21-26 July 2016, Honolulu, Hawaii : proceedings. Unter Mitarbeit von Rama Chellappa, Zhengyou Zhang und Anthony Hoogs. 2017 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Honolulu, HI, 7/21/2017 - 7/26/2017. IEEE Conference on Computer Vision and Pattern Recognition; Institute of Electrical and Electronics Engineers; IEEE/CVF Conference on Computer Vision and Pattern Recognition; CVPR. Piscataway, NJ: IEEE, S. 5679–5688.
Zhang, Jiawei; Jiao, Jianbo; Chen, Mingliang; Qu, Liangqiong; Xu, Xiaobin; Yang, Qingxiong (2016): 3D Hand Pose Tracking and Estimation Using Stereo Matching. Online verfügbar unter http://arxiv.org/pdf/1610.07214v1.

## Slide 11: Sources
Liu, Zhi; Zhang, Chenyang; Tian, Yingli (2016): 3D-based Deep Convolutional Neural Network for action recognition with depth sequences. In: Image and Vision Computing 55, S. 93–100. DOI: 10.1016/j.imavis.2016.04.004.
Hoang, Nguyen Ngoc; Lee, Guee-Sang; Kim, Soo-Hyung; Yang, Hyung-Jeong (2018): A Real-time Multimodal Hand Gesture Recognition via 3D Convolutional Neural Network and Key Frame Extraction. In: Unknown (Hg.): Proceedings of the 2018 International Conference on Machine Learning and Machine Intelligence - MLMI2018. the 2018 International Conference. Ha Noi, Viet Nam, 28.09.2018 - 30.09.2018. New York, New York, USA: ACM Press, S. 32–37.
Farooq, Adnan; Won, Chee Sun (2015): A Survey of Human Action Recognition Approaches that use an RGB-D Sensor. In: IEIE Transactions on Smart Processing and Computing 4 (4), S. 281–290. DOI: 10.5573/IEIESPC.2015.4.4.281.
Wang, Pichao; Li, Wanqing; Gao, Zhimin; Zhang, Jing; Tang, Chang; Ogunbona, Philip O. (2016): Action Recognition From Depth Maps Using Deep Convolutional Neural Networks. In: IEEE Trans. Human-Mach. Syst. 46 (4), S. 498–509. DOI: 10.1109/THMS.2015.2504550.
Xin, Miao; Zhang, Hong; Wang, Helong; Sun, Mingui; Yuan, Ding (2016): ARCH: Adaptive recurrent-convolutional hybrid networks for long-term action recognition. In: Neurocomputing 178, S. 87–102. DOI: 10.1016/j.neucom.2015.09.112.

## Slide 12: Sources
Szeliski, Richard (1989): Bayesian modeling of uncertainty in low-level vision (The Kluwer international series in engineering and computer science).
Yuan, Shanxin; Ye, Qi; Stenger, Bjorn; Jain, Siddhant; Kim, Tae-Kyun (2017): BigHand2.2M Benchmark: Hand Pose Dataset and State of the Art Analysis. Online verfügbar unter http://arxiv.org/pdf/1704.02612v2.
Sun, Xiao; Wei, Yichen; Liang, Shuang; Tang, Xiaoou; Sun, Jian (2015): Cascaded hand pose regression. In: 2015 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). - 12 June 2015, Boston, MA. 2015 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Boston, MA, USA, 6/7/2015 - 6/12/2015. Institute of Electrical and Electronics Engineers; IEEE Conference on Computer Vision and Pattern Recognition; CVPR. Piscataway, NJ: IEEE, S. 824–832.
Hafiz, Abdul Rahman; Al-Nuaimi, Ahmed Yarub; Amin, Md. Faijul; Murase, Kazuyuki (2015): Classification of Skeletal Wireframe Representation of Hand Gesture Using Complex-Valued Neural Network. In: Neural Processing Letters 42 (3), S. 649–664. DOI: 10.1007/s11063-014-9379-0.
Szeliski, Richard (2011): Computer vision. Algorithms and applications (Texts in computer science).

## Slide 13: Sources
Szeliski, Richard (2011): Computer Vision. Algorithms and Applications. London: Springer London (Texts in computer science).
Szeliski, Richard (2010): Computer Vision. Algorithms and Applications. 1. Aufl. Guildford, Surrey: Springer London (Texts in computer science).
Cremers, Daniel; Reid, Ian; Saito, Hideo; Yang, Ming-Hsuan (Hg.) (2015): Computer Vision -- ACCV 2014. Cham: Springer International Publishing (Lecture Notes in Computer Science).
Cremers, Daniel; Reid, Ian; Saito, Hideo; Yang, Ming-Hsuan (Hg.) (2015): Computer Vision -- ACCV 2014. Cham: Springer International Publishing (Lecture Notes in Computer Science).
Fitzgibbon, Andrew; Lazebnik, Svetlana; Perona, Pietro; Sato, Yoichi; Schmid, Cordelia (Hg.) (2012): Computer vision - ECCV 2012. 12th European Conference on Computer Vision, Florence, Italy, October 7 - 13, 2012 ; proceedings, part VI. ECCV; European Conference on Computer Vision. Berlin: Springer (Lecture Notes in Computer Science, 7577).

## Slide 14: Sources
Núñez, Juan C.; Cabido, Raúl; Pantrigo, Juan J.; Montemayor, Antonio S.; Vélez, José F. (2018): Convolutional Neural Networks and Long Short-Term Memory for skeleton-based human activity and hand gesture recognition. In: Pattern Recognition 76, S. 80–94. DOI: 10.1016/j.patcog.2017.10.033.
Li, Yuan; Wang, Xinggang; Liu, Wenyu; Feng, Bin (2018): Deep attention network for joint hand gesture localization and recognition using static RGB-D images. In: Information Sciences 441, S. 66–78. DOI: 10.1016/j.ins.2018.02.024.
Pfister, Tomas; Simonyan, Karen; Charles, James; Zisserman, Andrew (2015): Deep Convolutional Neural Networks for Efficient Pose Estimation in Gesture Videos. In: Daniel Cremers, Ian Reid, Hideo Saito und Ming-Hsuan Yang (Hg.): Computer Vision -- ACCV 2014, Bd. 9003. Cham: Springer International Publishing (Lecture Notes in Computer Science), S. 538–552.
Di Wu; Pigou, Lionel; Kindermans, Pieter-Jan; Le, Nam Do-Hoang; Shao, Ling; Dambre, Joni; Odobez, Jean-Marc (2016): Deep Dynamic Neural Networks for Multimodal Gesture Segmentation and Recognition. In: IEEE transactions on pattern analysis and machine intelligence 38 (8), S. 1583–1597. DOI: 10.1109/TPAMI.2016.2537340.
Devineau, Guillaume; Moutarde, Fabien; Xi, Wang; Yang, Jie (2018): Deep Learning for Hand Gesture Recognition on Skeletal Data. In: 13th IEEE International Conference on Automatic Face and Gesture Recognition. FG 2018 : 15-19 May 2018, Xi'an, China : proceedings. 2018 13th IEEE International Conference on Automatic Face & Gesture Recognition (FG 2018). Xi'an, 5/15/2018 - 5/19/2018. IEEE International Conference on Automatic Face and Gesture Recognition; Institute of Electrical and Electronics Engineers; FG. Piscataway, NJ: IEEE, S. 106–113.

## Slide 15: Sources
Malik, Jameel; Elhayek, Ahmed; Nunnari, Fabrizio; Varanasi, Kiran; Tamaddon, Kiarash; Heloir, Alexis; Stricker, Didier (2018): DeepHPS: End-to-end Estimation of 3D Hand Pose and Shape by Learning from Synthetic Depth. Online verfügbar unter http://arxiv.org/pdf/1808.09208v1.
Yuan, Shanxin; Garcia-Hernando, Guillermo; Stenger, Bjorn; Moon, Gyeongsik; Chang, Ju Yong; Lee, Kyoung Mu et al. (2017): Depth-Based 3D Hand Pose Estimation: From Current Achievements to Future Goals. Online verfügbar unter http://arxiv.org/pdf/1712.03917v2.
Wu, Chih-Hung; Chen, Wei-Lun; Lin, Chang Hong (2016): Depth-based hand gesture recognition. In: Multimed Tools Appl 75 (12), S. 7065–7086. DOI: 10.1007/s11042-015-2632-3.
Supančič, James Steven; Rogez, Grégory; Yang, Yi; Shotton, Jamie; Ramanan, Deva (2018): Depth-Based Hand Pose Estimation: Methods, Data, and Challenges. In: Int J Comput Vis 126 (11), S. 1180–1198. DOI: 10.1007/s11263-018-1081-7.
Melax, Stan; Keselman, Leonid; Orsten, Sterling (2017): Dynamics Based 3D Skeletal Hand Tracking. Online verfügbar unter http://arxiv.org/pdf/1705.07640v1.

## Slide 16: Sources
Oikonomidis, Iason; Kyriazis, Nikolaos; Argyros, Antonis (2011): Efficient model-based 3D tracking of hand articulations using Kinect. In: Jesse Hoey (Hg.): Proceedings of the British Machine Vision Conference 2011. BMVC 2011, the 22nd British Machine Vision Conference, University of Dundee, 29 August-2 September 2011. British Machine Vision Conference 2011. Dundee. British Machine Vision Conference; BMVC. Durham: BMVA Press, 101.1-101.11.
Kang, Sing Bing; Szeliski, Richard: Extracting View-Dependent Depth Maps from a Collection of Images.
Garcia-Hernando, Guillermo; Yuan, Shanxin; Baek, Seungryul; Kim, Tae-Kyun (2017): First-Person Hand Action Benchmark with RGB-D Videos and 3D Hand Pose Annotations. Online verfügbar unter http://arxiv.org/pdf/1704.02463v2.
Ohn-Bar, Eshed; Trivedi, Mohan Manubhai (2014): Hand Gesture Recognition in Real Time for Automotive Interfaces: A Multimodal Vision-Based Approach and Evaluations. In: IEEE Trans. Intell. Transport. Syst. 15 (6), S. 2368–2377. DOI: 10.1109/TITS.2014.2337331.
Simon, Tomas; Joo, Hanbyul; Matthews, Iain; Sheikh, Yaser (2017): Hand Keypoint Detection in Single Images using Multiview Bootstrapping. Online verfügbar unter http://arxiv.org/pdf/1704.07809v1.

## Slide 17: Sources
Keskin, Cem; Kıraç, Furkan; Kara, Yunus Emre; Akarun, Lale (2012): Hand Pose Estimation and Hand Shape Classification Using Multi-layered Randomized Decision Forests. In: Andrew Fitzgibbon, Svetlana Lazebnik, Pietro Perona, Yoichi Sato und Cordelia Schmid (Hg.): Computer vision - ECCV 2012. 12th European Conference on Computer Vision, Florence, Italy, October 7 - 13, 2012 ; proceedings, part VI, Bd. 7577. Berlin: Springer (Lecture Notes in Computer Science, 7577), S. 852–863.
Hampali, Shreyas; Oberweger, Markus; Rad, Mahdi; Lepetit, Vincent (2019): HO-3D: A Multi-User, Multi-Object Dataset for Joint 3D Hand-Object Pose Estimation. Online verfügbar unter http://arxiv.org/pdf/1907.01481v1.
Poier, Georg; Roditakis, Konstantinos; Schulter, Samuel; Michel, Damien; Bischof, Horst; Argyros, Antonis A. (2015): Hybrid One-Shot 3D Hand Pose Estimation by Exploiting Uncertainties. In: Xianghua Xie, Mark W. Jones und Gary K. L. Tam (Hg.): Proceedings of the British Machine Vision Conference 2015. BMVC 2015, 7-10 September, Swansea, UK. British Machine Vision Conference 2015. Swansea. British Machine Vision Conference; BMVC. Durham: BMVA Press, 182.1-182.14.
Institute of Electrical and Electronics Engineers; IEEE Computer Society; IEEE Conference on Computer Vision and Pattern Recognition; CVPR (2013): IEEE Conference on Computer Vision and Pattern Recognition (CVPR), 2013. 23 - 28 June 2013, Portland, Oregon, USA ; proceedings. 2013 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Portland, OR, USA, 6/23/2013 - 6/28/2013. Piscataway, NJ: IEEE.
Szeliski, Richard (2006): Image alignment and stitching. A Tutorial. Hanover Mass. u.a.: Now Publ (Foundations and trends in computer graphics and vision, 2,1).

## Slide 18: Sources
Sridhar, Srinath; Oulasvirta, Antti; Theobalt, Christian (2013): Interactive Markerless Articulated Hand Motion Tracking using RGB and Depth Data. In: Proceedings of the IEEE International Conference on Computer Vision (ICCV). Online verfügbar unter http://handtracker.mpi-inf.mpg.de/projects/handtracker_iccv2013/.
Fei-Fei, Li: Knowledge transfer in learning to recognize visual objects classes.
Zimmermann, Christian; Brox, Thomas (2017): Learning to Estimate 3D Hand Pose from Single RGB Images. Online verfügbar unter http://arxiv.org/pdf/1705.01389v3.
Liu, Qiong; Lienhart, Rainer; Wang, Haohong; Chen, Sheng-Wei "Kuan-Ta"; Boll, Susanne; Chen, Phoebe et al. (Hg.) (2017): MM'17. Proceedings of the 2017 ACM Multimedia Conference : October 23-27, 2017, Amsterdam, the Netherlands. Unter Mitarbeit von Qiong Liu, Rainer Lienhart und Haohong Wang. the 2017 ACM. Mountain View, California, USA, 10/23/2017 - 10/27/2017. ACM Multimedia Conference; Association for Computing Machinery; ACM Multimedia; MM. New York, NY, USA: ACM Association for Computing Machinery.
Lin, John; Wu, Ying; Huang, T. S. (2000): Modeling the constraints of human hand motion. In: Proceedings, Workshop on Human Motion. 7-8 December 2000, Austin, Texas. Workshop on Human Motion. Los Alamitos, CA, USA, 7-8 Dec. 2000. Workshop on Human Motion; IEEE Computer Society. Los Alamitos, Calif: IEEE Computer Society, S. 121–126.

## Slide 19: Sources
Patrona, Fotini; Chatzitofis, Anargyros; Zarpalas, Dimitrios; Daras, Petros (2018): Motion analysis: Action detection, recognition and evaluation based on motion capture data. In: Pattern Recognition 76, S. 612–622. DOI: 10.1016/j.patcog.2017.12.007.
Maddison, Chris J.; Huang, Aja; Sutskever, Ilya; Silver, David (2014): Move Evaluation in Go Using Deep Convolutional Neural Networks. Online verfügbar unter http://arxiv.org/pdf/1412.6564v2.
Stark, Michael: On knowledge transfer in object class recognition. Darmstadt, Techn. Univ., Diss., 2010.
Molchanov, Pavlo; Yang, Xiaodong; Gupta, Shalini; Kim, Kihwan; Tyree, Stephen; Kautz, Jan (2016 - 2016): Online Detection and Classification of Dynamic Hand Gestures with Recurrent 3D Convolutional Neural Networks. In: 2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). 2016 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Las Vegas, NV, USA, 27.06.2016 - 30.06.2016: IEEE, S. 4207–4215.
Li, Cheng; Kitani, Kris M. (2013): Pixel-Level Hand Detection in Ego-centric Videos. In: IEEE Conference on Computer Vision and Pattern Recognition (CVPR), 2013. 23 - 28 June 2013, Portland, Oregon, USA ; proceedings. 2013 IEEE Conference on Computer Vision and Pattern Recognition (CVPR). Portland, OR, USA, 6/23/2013 - 6/28/2013. Institute of Electrical and Electronics Engineers; IEEE Computer Society; IEEE Conference on Computer Vision and Pattern Recognition; CVPR. Piscataway, NJ: IEEE, S. 3570–3577.

## Slide 20: Sources
Proceedings IEEE Virtual Reality 2001 (2001). IEEE Virtual Reality 2001. Yokohama, Japan, 13-17 March 2001: IEEE Comput. Soc.
Proceedings IEEE Virtual Reality 2001 (2001). IEEE Virtual Reality 2001. Yokohama, Japan, 13-17 March 2001: IEEE Comput. Soc.
Unknown (Hg.) (2018): Proceedings of the 2018 International Conference on Machine Learning and Machine Intelligence - MLMI2018. the 2018 International Conference. Ha Noi, Viet Nam, 28.09.2018 - 30.09.2018. New York, New York, USA: ACM Press.
Proceedings of the 5th international conference on devlopment and learning ICDL 2006. Indiana University, Bloomington, IN : May 31 - June 3rd, 2006 (2006). [Bloomington, Ind.]: Department of Psychological and Brain Sciences, Indiana University.
Hoey, Jesse (Hg.) (2011): Proceedings of the British Machine Vision Conference 2011. BMVC 2011, the 22nd British Machine Vision Conference, University of Dundee, 29 August-2 September 2011. British Machine Vision Conference 2011. Dundee. British Machine Vision Conference; BMVC. Durham: BMVA Press.

## Slide 21: Sources
Xie, Xianghua; Jones, Mark W.; Tam, Gary K. L. (Hg.) (2015): Proceedings of the British Machine Vision Conference 2015. BMVC 2015, 7-10 September, Swansea, UK. British Machine Vision Conference 2015. Swansea. British Machine Vision Conference; BMVC. Durham: BMVA Press.
Proceedings of the IEEE International Conference on Computer Vision (ICCV) (2013).
Workshop on Human Motion; IEEE Computer Society (2000): Proceedings, Workshop on Human Motion. 7-8 December 2000, Austin, Texas. Workshop on Human Motion. Los Alamitos, CA, USA, 7-8 Dec. 2000. Los Alamitos, Calif: IEEE Computer Society.
Ge, Liuhao; Liang, Hui; Yuan, Junsong; Thalmann, Daniel (2019): Real-Time 3D Hand Pose Estimation with 3D Convolutional Neural Networks. In: IEEE transactions on pattern analysis and machine intelligence 41 (4), S. 956–970. DOI: 10.1109/TPAMI.2018.2827052.
Tang, Danhang; Yu, Tsz-Ho; Kim, Tae-Kyun (2014): Real-Time Articulated Hand Pose Estimation Using Semi-supervised Transductive Regression Forests. In: 2013 IEEE International Conference on Computer Vision. 1-8 December 2013. 2013 IEEE International Conference on Computer Vision (ICCV). Sydney, Australia, 12/1/2013 - 12/8/2013. New York: IEEE, S. 3224–3231.

## Slide 22: Sources
Tompson, Jonathan; Stein, Murphy; Lecun, Yann; Perlin, Ken (2014): Real-Time Continuous Pose Recovery of Human Hands Using Convolutional Networks. In: ACM Trans. Graph. 33 (5), S. 1–10. DOI: 10.1145/2629500.
Köpüklü, Okan; Gunduz, Ahmet; Kose, Neslihan; Rigoll, Gerhard (2019): Real-time Hand Gesture Detection and Classification Using Convolutional Neural Networks. Online verfügbar unter http://arxiv.org/pdf/1901.10323v2.
Lu, Bao-Liang; Zhang, Liqing; Kwok, James; Hafiz, Abdul Rahman; Amin, Md. Faijul; Murase, Kazuyuki (Hg.) (2011): Real-Time Hand Gesture Recognition Using Complex-Valued Neural Network (CVNN). Neural Information Processing. Berlin, Heidelberg: Springer Berlin Heidelberg.
Shotton, Jamie; Fitzgibbon, Andrew; Blake, Andrew; Kipman, Alex; Finocchio, Mark; Moore, Bob; Sharp, Toby (2011): Real-Time Human Pose Recognition in Parts from a Single Depth Image. Online verfügbar unter https://www.microsoft.com/en-us/research/wp-content/uploads/2016/02/BodyPartRecognition.pdf.
Sato, Y.; Saito, M.; Koike, H. (2001): Real-time input of 3D pose and gestures of a user's hand and its applications for HCI. In: Proceedings IEEE Virtual Reality 2001. IEEE Virtual Reality 2001. Yokohama, Japan, 13-17 March 2001: IEEE Comput. Soc, S. 79–86.

## Slide 23: Sources
Uni Freiburg: Rendered Handpose Dataset: Uni Freiburg. Online verfügbar unter https://lmb.informatik.uni-freiburg.de/resources/datasets/RenderedHandposeDataset.en.html.
Ge, Liuhao; Liang, Hui; Yuan, Junsong; Thalmann, Daniel (2016): Robust 3D Hand Pose Estimation in Single Depth Images: from Single-View CNN to Multi-View CNNs. Online verfügbar unter http://arxiv.org/pdf/1606.07253v3.
Malik, Jameel; Elhayek, Ahmed; Stricker, Didier (2017): Simultaneous Hand Pose and Skeleton Bone-Lengths Estimation from a Single Depth Image. Online verfügbar unter http://arxiv.org/pdf/1712.03121v1.
Li, Yong; He, Zihang; Ye, Xiang; He, Zuguo; Han, Kangrong (2019): Spatial temporal graph convolutional networks for skeleton-based dynamic hand gesture recognition. In: J Image Video Proc. 2019 (1), S. 404. DOI: 10.1186/s13640-019-0476-x.
Jones, Michael J.; Rehg, James M. (2002): Statistical Color Models with Application to Skin Detection. In: Int J Comput Vis 46 (1), S. 81–96. DOI: 10.1023/A:1013200319198.

## Slide 24: Sources
Scharstein, Daniel; Szeliski, Richard: Stereo Matching with Nonlinear Diffusion.
Malik, Jameel; Elhayek, Ahmed; Stricker, Didier (2018): Structure-Aware 3D Hand Pose Regression from a Single Depth Image. In: Patrick Bourdot, Sue Cobb, Victoria Interrante, Hirokazu kato und Didier Stricker (Hg.): Virtual reality and augmented reality. 15th EuroVR International Conference, EuroVR 2018, London, UK, October 22–23, 2018 : proceedings, Bd. 11162. Cham: Springer (Lecture Notes in Computer Science, 11162), S. 3–17.
Yuan, Shanxin; Ye, Qi; Garcia-Hernando, Guillermo; Kim, Tae-Kyun (2017): The 2017 Hands in the Million Challenge on 3D Hand Pose Estimation. Online verfügbar unter http://arxiv.org/pdf/1707.02237v1.
Bourdot, Patrick; Cobb, Sue; Interrante, Victoria; kato, Hirokazu; Stricker, Didier (Hg.) (2018): Virtual reality and augmented reality. 15th EuroVR International Conference, EuroVR 2018, London, UK, October 22–23, 2018 : proceedings. Springer International Publishing AG; EuroVR. Cham: Springer (Lecture Notes in Computer Science, 11162).

## Slide 25: Masterfolie (über: Ansicht – Master – Folienmaster)
Die Masterfolie wird genutzt, um grundlegende Elemente der Präsentation festzulegen und ggf. zu ändern.
Folgende Elemente können Sie in der Normalansicht individuell eintragen:
  Inhaltsbereich:
    Präsentationsüberschrift
    Unterüberschrift
    Fakultätsbezeichnung
    Bildaustausch (graue Lasche am rechten Folienrand – zum leichteren Austausch)
  Fußzeile (über: Ansicht – Kopf- und Fußzeile)

## Slide 26: Folientitel: Arial 24pt fett 2-zeilig: Arial 20pt fett
Fließtext: Arial 24pt regular
Fußzeile: Arial 9pt regular
Seitenzahl: Arial 9pt fett
Aufzählungspunkte, falls nicht auf Folie vorhanden:
  Format – Nummerierung- und Aufzählungszeichen – Bild – Importieren
  Die Datei „kit-point.png“ auswählen
  Größe: „70% vom Text“
Farben:
  Sind bereits voreingestellt. Sie erhalten automatisch die KIT-Farbpalette

## Slide 27: Generelle Hinweise
Das Foliendesign sollte nicht geändert werden
Wenn Sie aus einem anderen Office-Programm Texte kopieren, wird Powerpoint die Formatierungen beibehalten. Hier müssen Sie die Texte evtl. neu formatieren.
Grundlegende Elemente wie diese im grauen KIT-Rahmen, das KIT-Logo oder die Platzhalter sollten in der Position nicht verändert oder gelöscht werden.

## Slide 28: Tipps zur Verwendung von Powerpoint
Seitenaufbau
  Text und Grafiken: Diese Elemente sollten gezielt und zurückhaltend eingesetzt werden. Empfohlen werden zehn Worte pro Zeile und fünf Zeilen pro Folie.
  Zahlen und Daten Effektive PowerPoint-Präsentationen enthalten wenig Zahlen: ausführliche Daten können Sie nach der Präsentation auf Handouts verteilen.